Mechanical engineering

1.	When a house is under construction, builders often nail asphalt shingles to the roof.

a)	Which components hold the shingles on the roof?

b)	What is the mechanical function of these components?

[		/2]

2.	Football is a sport that requires a lot of equipment, including a helmet. Inside the helmet is a layer of flexible padding to protect the player’s head. It is held in place with glue. What are the characteristics of the link between the padding and the helmet? Explain each characteristic.

a)	Direct or indirect?

b)	Rigid or flexible?

c)	Removable or non-removable?

d)	Complete or partial?

[		/8]

3.	Helmets are mandatory not only in football; they are also required in ice hockey. One of the differences between football helmets and hockey helmets lies in their wire face masks. The masks on hockey helmets can usually be raised, but not the masks on football helmets.

a)	Given that the mask is usually attached to the hockey helmet with two screws and two nuts, what are the characteristics of this link? Explain each characteristic.

A.	Direct or indirect?

B.	Rigid or flexible?

C.	Removable or non-removable?

D.	Complete or partial?

b)	How many degrees of freedom does the mask have in relation to the helmet? Explain your answer.

[		/10]

4.	Safety bolts like the one illustrated below are used to lock doors.

Bolt	Housing

a)	What are the characteristics of the link between the bolt and the housing? Explain each characteristic.

A.	Direct or indirect?

B.	Rigid or flexible?

C.	Removable or non-removable?

D.	Complete or partial?

b)	How many degrees of freedom does the bolt in this object have? Explain your answer.

[		/10]

5.	During a family breakfast, you explain that there are three main types of guiding. You use the jar of peanut butter with its screw-on lid, the cutlery drawer, the refrigerator door and the kitchen scissors as examples. Which type of guiding does each of these objects demonstrate?

a)	jar of peanut butter

b)	cutlery drawer

c)	refrigerator door

d)	kitchen scissors

[		/4]

6.	During a car race, your know-it-all uncle comments continually on the adhesion of the tires to the track. For each remark, write whether it is true or false and identify the factor causing the strength of adhesion between the surfaces to vary.

a)	“They wasted a lot of money renovating this racetrack. As if covering it with asphalt instead of concrete would make any difference in the cars’ performances! It doesn’t change a thing!”

b)	“Brrrr! It’s so cold! It’s a good thing it’s supposed to clear up and get warmer this afternoon. That will help the tires adhere to the track better.”

c)	“Yesterday, I took my old Bonneville out on the track. It was losing a little oil. I hope there isn’t any left on the track surface because that could make the cars skid and cause an accident.”

d)	“To think that they allowed an increase in the weight of the cars’ rear spoilers to prevent skidding. As if putting more weight on a tire makes it adhere better to the track! That makes no sense at all.”

e)	“Why is that car starting the race with smooth tires? The track’s all wet from the rain. The mechanics should have put ribbed-tread wheels on the car to keep it from skidding.”

[		/10]

7.	For a study on motion transmission, you have been asked to provide information on the main systems that perform this mechanical function. For each diagram below:

a)	Name the motion transmission system.

b)	Write “yes” or “no” regarding the possibility of reversibility.

c)	Complete the diagram by indicating the direction of rotation of each of the driver and driven components in the system.

A

Name of the system:	Worm and worm gear system

Possibility of reversibility:	No

B

Name of the system:	Friction gear system

Possibility of reversibility:	Yes

C

Name of the system:	Gear train

Possibility of reversibility:	Yes

D

Name of the system:	Belt and pulley system

Possibility of reversibility:	Yes

E

Name of the system:	Chain and sprocket system

Possibility of reversibility:	Yes

[		/20]

8.	One characteristic an engineer may look for in the design of a technical object is a significant change in rotational speed between the parts. The two systems below have been proposed to meet this purpose.

System 1	System 2

a)	Which type of motion transmission systems are they?

b)	In which system is the change in rotational speed between the gears greater? Explain your answer.

[		/4]

9.	A company has lost its computer data on the rotational speed of the B components in the systems below. Using the information provided in the drawings of these systems, calculate the rotational speed of the B components.

a)	b)

B	A	A	B

15 turns/minute	30 turns/minute

c)	d)

Diameter 
	= 4 cm

A	B	A	B

Diameter = 10 cm

Diameter = 20 cm 	Diameter = 20 cm

60 turns/minute	25 turns/minute

[		/8]

10.	You are presented with the drawing 
opposite for the design of a small vehicle 
operating on a spark-ignition engine.

a)	Does this drawing represent a motion 
transmission or a motion transformation 
system? Explain your answer.

b)	What is the name of this type of system?

c)	Name each of the numbered parts.

1:

2:

3:

d)	What does part 3 do?

[		/9]

11.	Later during the same vehicle design process, you are presented with the steering system illustrated below.

a)	Does this drawing represent a motion 
transmission or a motion transformation 
system? Explain your answer.

b)	What is the name of this type of system?

c)	Name each of the numbered parts.

1:

2:

[		/5]

[		/90]

# Text boxes

ANSWER KEY

EST

Concept evaluations by chapter

CHAPTER 13

The nails

Linking

Indirect, because a linking component is needed to attach the padding to the helmet.

Flexible, because the surface of the padding can be deformed.

Non-removable, because if someone tries to remove the padding, the linking component and possibly also the padding would break.

Complete, because the padding cannot move independently of the helmet.

Indirect, because linking components are needed to attach the mask to the helmet.

Rigid, because neither the linking components nor the surfaces of the linked parts can be deformed.

Removable, because the mask can be raised without damaging the helmet, the mask or the linking components.

Partial, because the mask can move independently of the helmet.

EST

The mask has only one degree of freedom because it can make one rotational motion independently of the helmet, up and down.

Direct, because there is no linking component between the bolt and the housing.

Rigid, because the surfaces of the parts cannot be deformed.

Partial, because the bolt moves independently of the housing.

Non-removable, because it is impossible to separate the bolt from the housing without damaging one of the two parts.

EST

The bolt has two degrees of freedom because it can move from left to right (translational motion) and from top to bottom (rotational motion).

Helical guiding

Translational guiding

Rotational guiding

Rotational guiding

EST

False. The nature of the materials in contact

True. The temperature

True. The presence of a lubricant

False. The perpendicular force exerted by one surface on another

True. The state of the surfaces in contact

Gear trains

The speed decreases more in system 2 because there is a greater difference in the number of teeth on the two gears.

7.5 turns/minute	45 turns/minute

120 turns/minute	125 turns/minute

Piston

Crankshaft

It is a motion transformation system because it transforms a translational motion into a rotational motion.

It is a slider-crank mechanism.

Connecting rod

Crank

Cylinder

It acts as a guiding component for the translational motion of the piston.

It is a motion transformation system because it transforms a rotational motion into a translational motion.

It is a rack and pinion system.

Rack

Pinion